ООО «Торговый Дом «Прометей»

142410, г. Ногинск, Московская область, ул. Бетонная, д.3

Контакты: (495) 979-76-05

(977) 316-76-05,

(903) 100-34-47

ICQ: 408280786

E-mail: info@tdprometey.ru

Сайт: www.tdprometey.ru

# Каталог по пневмоприводам, электроприводам, позиционерам, датчикам, креплениям

# Пневмоприводы, электроприводы, позиционеры, датчики, крепления

| 4405 - Пневмотический привод одинарного действия: воздух пружина С - Р | DN Размер A B C Mk Mk [AIR-S bar] | [SPRING] SR 050 140,5 69 70,5 6,5 Nm 6,0 Nm SR 100 158,5 85 83 11,2 Nm 10,0 Nm SR 200 210,5 102 94,5 22,7 Nm 20,3 Nm SR 250 247,5 115 106,3 33,3 Nm 30,0 Nm SR 300 268,5 127 123 54,2 Nm 48,6 Nm SR 400 345,0 145 141 117,0 Nm 102,0 Nm |
| --- | --- | --- |

| 4410 - Пневмотический привод двойного действия: воздух - воздух D - A | DN Размер A B C Mk [AIR-S bar] DA 050 140,5 69 70,5 14,8 Nm DA 100 158,5 85 83 26,4 Nm DA 200 210,5 102 94,5 56,1 Nm DA 250 247,5 115 106,3 85,4 Nm DA 300 268,5 127 123 133,0 Nm DA 400 345,0 145 141 288,0 Nm |
| --- | --- |

| 4414 - Держатель пневмопривода | DN Размер B2 D1 D2 L1 кг 25 17,6 6 9 30,3 0,2 32 17,6 6 9 30,3 0,3 40 17,6 6 9 30,3 0,3 50 17,6 6 9 30,3 0,3 65 17,6 6 9 30,3 0,3 80 17,6 6 9 30,3 0,4 100 17,6 6 9 30,3 0,4 Только для 4415, 4420 |
| --- | --- |

| 4415 - Вертикальный пневмотический привод двойного действия: воздух - воздух | DN Размер D1 D2 B L1 кг 25 89 R 1/8" 9,5 175 2,5 32 89 R 1/8" 9,5 175 2,5 40 89 R 1/8" 9,5 175 2,5 50 89 R 1/8" 9,5 175 2,5 65 89 R 1/8" 9,5 175 2,5 80 115 R 1/8" 9,5 175 4,1 100 115 R 1/8" 9,5 175 4,1 125 129 R 1/8" 14,0 175 7,2 150 129 R 1/8" 14,0 175 7,2 |
| --- | --- |

| 4420 - Вертикальный пневмотический привод одинарного действия: воздух - пружина С - Р | DN Размер D1 D2 B L1 кг 25 89 R 1/8" 9,5 175 3,1 32 89 R 1/8" 9,5 175 3,1 40 89 R 1/8" 9,5 175 3,1 50 89 R 1/8" 9,5 175 3,1 65 89 R 1/8" 9,5 175 3,1 80 115 R 1/8" 9,5 175 4,7 100 115 R 1/8" 9,5 175 4,7 125 129 R 1/8" 14,0 175 9,3 150 129 R 1/8" 14,0 175 9,3 |
| --- | --- |

| 4422 - Переключатель | DN Размер L1 кг 25 - 100 92 0,03 125 - 200 72 0,04 |
| --- | --- |

| 4423 - Держатель включателя | DN Размер D1 D2 кг 25 - 100 18,3 6 0,04 12,3 6 0,04 125 - 200 18,3 9 0,05 12,3 9 0,05 |
| --- | --- |

| 4427 - Электромагнитный вентиль (прямой) | DN Description - Solenoid valve directly operated with 3/2 - ways function - All entrles have G 1/8" - Single stable version - Body Aluminium anodised, with minimal external dimensions - Piston Stainless steel AISI 303 - Sealings NBR - Screws Stainless steel AISI 304 Air entry G 1/8" Dimensions 1,3 mm Air pressure 0 - 10 bar Temperature -10°C- +70°C Enclosure PI 65 - DIN 40050 Voltage 24V AC 24V DC 230V AC Power consumption SVA 3W 5VA Air flow 50 l/min |
| --- | --- |
| 4430 - Электромагнитный ветниль (клапан) | DN Air entry G 1/8" Dimensions 1,3 mm Air pressure 0 - 10 bar Temperature -10°C- +70°C Enclosure PI 65 - DIN 40050 Voltage 24V AC 24V DC 230V AC Power consumption SVA 3W 5VA Air flow 50 l/min Description - Solenoid valve NAMUR with combined 5/2 - and 3/2 - ways function ith standard coil and connector - Easy change over from 5/2 - to 3/2 - ways operation by innovative sealing plate - Single stable version - Manual override as standard - Body Aluminium anodised, with minimal external dimensions - NAMUR copling plate PA6 - 30% Glass fibre - Piston Stainless steel AISI 303, Sealing NBR, Screws Stainless steel AISI 304 |
| 4436 - Индуктивный датчик | DN Размер М 12 |
| 4437 - Держатель индуктивного датчика | DN Размер |
| 4445 - Концевой индукционный позиционер | DN - компактный блок концевых указателей положения из поликарбоната или вестамида с прозрачной крышкой из поликарбоната - также возможен по заказу с элементом регулирования давления во избежаниие образования конденсата. Цены по запросу - Защита корпуса IP65 согласно стандарту DIN 40050 - Уплотнение кабеля черного или синего цвета М 20 x 1,5 (для кабеля ? 6-12 мм) - Уплотнения изготовлены из EPDM ( каучук на основе сополимера этилена, пропилена и диенового мономера) и NBR (бутадиен - нитрильный каучук), винты и болты изготовлены из AISI 304 - Кронштейны, регулируемые по высоте и длине, изготовлены из AISI 304 ( специальный шаг между отверстиями и высота стержня - по запросу и частично на складе) - Стержень изготовлен из черного полиамида или нержавеющей стали AISI 303 |
| 4442 - Глушитель шума | DN Размер G L G 1/8 G 1/8" 21,5 G 1/4 G 1/4" 26,5 |
| 4443 - Присоединение винтовое | DN Размер G D G 1/8 - 4 G 1/8" 4 G 1/8 - 6 G 1/8" 6 G 1/8 - 8 G 1/8" 8 G 1/8 - 10 G 1/8" 10 G 1/4 - 4 G 1/4" 4 G 1/4 - 6 G 1/4" 6 G 1/4 - 8 G 1/4" 8 G 1/4 - 10 G 1/4" 10 G 1/4 - 12 G 1/4" 12 |
| 4450 - Нипель внешний | DN Размер G1 G2 1/4 - 1/4 G 1/4" G 1/4" 1/4 - 1/8 G 1/4" G 1/8" 1/8 - 1/8 G 1/8" G 1/8" 3/8 - 3/8 G 3/8" G 3/8" |
| 4455 - Электропривод | DN Размер Typ Mk (Nm) SP 0 4 - 40 SP 0.1 16 - 50 SP 1 40 - 80 Диапазон температур: -25?C до 55?C |
| 4451 - Держатель индуктивного датчика | DN Размер |
| 4452 - Поворотный включатель | DN Размер |
| 4453 - Индуктивный датчик | DN Размер |
| 4454 - Кабельный разъём | DN General specification Number of poles 4 Construction type Socket, angled Electrical specification Operating voltage max. 60 V DC Operating current max. 4 A Volume resistance < 5 mohm Ambient conditions Ambient temperature -5...70?C(268...343 K) active -30...80?C(243...353 K) unmoved Degree of soilling 3 |
| 4481 - Позиционер GEMU | DN Werksoff: Aluminium beschichtet Zuluft: max. 6 bar Eingangssignal: 0/4 - 20 mA, 0 - 10 V Ausgangssignal: 0 -10 V, optional 4 - 20 mA Versorgungsspannung: 24 V DC Construction The digital electro-preumatic positioner detects the valve position with an external LongLife travel sensor. It has a solid housing with protected operating keys and an easy to read LCD display. The operating times can be set by integrated throttles. Connection and mounting to NAMUR is also possible. Features  Simple and left-explanatory menu  Automatic initialization function  Safety function during power or compressed air supply  No air consumption when idle  Protection class IP 65  3/4 - wire type Advantages  Separate mounting of positioner and travel sensor  Simple handling and commisioning  Simple electrical connection by detachable terminals  Automatic optimization of valve control during inititalization  Can be used with linear and quarter turn actuators  Operation with single and double acting actuators |
| 4482 - Датчик положения | DN Werkstoff: PAI, Poliamidimid Ausgangssignal ?3 KOhm |

| 4456 - Электропривод | DN Voltage 24V DC, 220V DC Enclocure IP 67 Maximum Torque 58 Nm Operating time 90° 14 sec |
| --- | --- |

| 4480 - Позиционер GEMU | DN Body Aluminium plastic-coated Seal EPDM, NBR, FKM Operating voltages 24 VDC +/- 10% Residual ripple max. 10% Setpoint setting 0/4 to 20mA and 0 to 5/10 V Input resistance 0/4 to 20 mA: 180 Ω0/4 to 20 mA: 180 Ω0/4 to 20 mA: 180 Ω0/4 to 20 mA: 180 Ω 0 to 5/10 mA: 19 k Ω 0/4 to 20 mA: 180 Ω 0 to 5/10 mA: 19 k Ω Analogue feedback 4-20 mA, 0-20 mA 0-10 V, 0-5 V Binary input galvanically isolated, 0-5 V = log “0”, 10-30 V = log “1” Binary output 2 Outputs (optional), galvanically separated Current limit 100 mA, Output will be synchronised when overloaded Control medium Neutral gases, air DIN ISO 8573-1 Dust concentration Class 5 (<40μm particle size) Particle density Class 5 (<10mg/m 3) Pressure condensation point Class 3 (<-20°C) Oil concentration Class 5 (<25mg/m 3) Ambient temperature 0 to +60°C Pilot air ports Threaded ports G 1/4 Supply pressure 1.4 to 7 bar Air supply fi lter Exchangeable (aperture size ~0.1mm) Actuator system single and double-acting to 150 l N/min. Air capacity 95 l N/min (with 1.4 bar 2)) for aeration and ventilation 150 l N/min (with 6 bar2)) for aeration and ventilation (Q Nn = 100 l N/min (acc. to the defi nition with decrease in pressure from 7 to 6 bar absolute) Position detection module Potentiometer, max. angle 180º Stroke range valve spindle min. 30º on the rotary shaft, depending on lever Installation as required, display above or sideways Type of protection IP 65/67 acc. to EN 60529 (NEMA4x in preparation) Power consumption < 5 W Multipole connection M12, 8-pin/4-pin; M8, 4-pin Cable gland 2xM20x1.5 (cable Ø10mm) on screw terminals (0.14-1.5 mm 2) Remote version 1xM12x1.5 (cable Ø3 to 6.5mm) Bus communication Profi bus DPV1 (optional) Inductive proximity switch on request Protection class 3 acc. to VDE 0580 Type of ignition protection II 3 G nA II B T4 (in preparation) II 3 D tD A22 T135° (in preparation) Conformity EMV2004/108/EG Approvals CSA (in preparation) Compact metal housing Graphic display with backlight Easy start-up Comprehensive range of additional software functions Profibus DPV 1 (optional) Assembly acc. to IEC 534-6 / VDI VDE 3845 |
| --- | --- |

# 4390 UNIV - Держатель пневмопривода

| DN | Размер |
| --- | --- |
|  | B1 | B2 | D1 | D2 | D3 | C |
| 50 | 17 | 30,5 | 50 | 7,5 | 6,5 | 9 |
| 65 | 17 | 30,5 | 50 | 7,5 | 6,5 | 9 |
| 80 | 17 | 30,5 | 50 | 7,5 | 6,5 | 9 |
| 100 | 17 | 30,5 | 50 | 7,5 | 6,5 | 9 |
| только для 4405, 4410, 4415, 4420 |

# 4394 - Поводок